## Slide 1
Autonomous Car Perception
Vision Pipeline • Camera Calibration • Depth Estimation
NAME
S. Kamali
REG. NO.
192524423
GUIDED BY
Mayuranathan

## Slide 2
INTRODUCTION
How a Self-Driving Car “Sees” the World
An autonomous car must continuously understand its surroundings — roads, pedestrians, vehicles, and traffic signs — to drive safely.
This understanding is built by three core computer-vision building blocks working together.
Vision Pipeline: the sequence of steps that turns raw camera frames into meaningful detections.
Camera Calibration: the process that ensures every image is geometrically accurate before analysis.
Depth Estimation: the technique that tells the car how far away each object is.
Vision Pipeline
Step 1 of 3
Camera Calibration
Step 2 of 3
Depth Estimation
Step 3 of 3
AUTONOMOUS CAR PERCEPTION
2

## Slide 3
A. VISION PIPELINE
From Raw Pixels to Real-World Understanding
Definition: The vision pipeline is the ordered sequence of image-processing and AI steps that convert raw camera video into detected roads, pedestrians, and signs.
1
Image
Acquisition
▶
2
Pre-
processing
▶
3
Feature
Extraction
▶
4
Object
Detection &
Classification
▶
5
Tracking &
Decision
Uses Convolutional Neural Networks (CNNs) such as YOLO or SSD for real-time detection.
Semantic segmentation labels every pixel (road, lane, sign, pedestrian) for fine-grained understanding.
Runs at 30+ frames per second so the car can react to fast-changing scenes.
AUTONOMOUS CAR PERCEPTION
3

## Slide 4
B. CAMERA CALIBRATION
Correcting the Camera's View of the World
Checkerboard
Calibration Pattern
Multiple images of a known pattern, taken from different angles, let software solve for the camera's internal and external parameters.
Why it's needed: Every lens introduces distortion (barrel/pincushion) and no two cameras are mounted identically — calibration corrects both.
Intrinsic parameters: Focal length, optical center, and lens distortion coefficients of the camera itself.
Extrinsic parameters: The camera's exact position and orientation relative to the vehicle body.
Result: Straight lines stay straight and pixel coordinates map accurately to real-world directions — essential before detection or depth math can be trusted.
AUTONOMOUS CAR PERCEPTION
4

## Slide 5
C. DEPTH ESTIMATION
Judging “How Far” — Not Just “What”
Definition: Depth estimation calculates the distance between the car and every detected object, turning a flat 2D image into a 3D understanding of the scene.
Stereo Vision
Two cameras, known baseline distance apart
Depth from pixel disparity between the pair
Similar to human binocular vision
LiDAR Fusion
Laser pulses measure exact distance directly
Fused with camera data for dense, labeled depth
Very accurate but higher cost
Why it matters: Distance data drives braking, lane changes, and collision avoidance — without it the car knows what is around it, but not whether it is safe.
AUTONOMOUS CAR PERCEPTION
5

## Slide 6
INTEGRATION
The Three Pieces Working as One System
1. Calibration
Corrects raw camera images so geometry is accurate
▶
2. Vision Pipeline
Detects roads, pedestrians, and traffic signs
▶
3. Depth Estimation
Adds distance to every detected object
▶
4. Safe Driving
Car plans steering, braking, and speed decisions
Together, these three stages let an autonomous car build a real-time, accurate, and geometrically correct picture of its environment.
AUTONOMOUS CAR PERCEPTION
6

## Slide 7
CHALLENGES & SUMMARY
Key Takeaways
Challenges
Poor lighting, rain, or fog can degrade camera-only detection accuracy.
Calibration must be re-checked periodically as vibration can shift camera position.
Stereo depth estimation is computationally heavy for real-time performance.
Sensor fusion (camera + LiDAR + radar) improves reliability over any single method.
Summary
Vision pipeline turns raw frames into detected roads, signs, and pedestrians.
Camera calibration guarantees those detections are geometrically trustworthy.
Depth estimation supplies the missing distance dimension for safe decisions.
Together they form the perception backbone of every self-driving system.
AUTONOMOUS CAR PERCEPTION
7

## Slide 8
Thank You
Questions & Discussion Welcome
S. Kamali • Reg. No. 192524423 • Guided by Mayuranathan